## Slide 1
Håvard Fjær Grip – Mars Helicopter Flight Control & Aerodynamics Lead
Jet Propulsion Laboratory, California Institute of Technology
Copyright 2019 California Institute of Technology. Government sponsorship acknowledged.
Mars Helicopter
Technology Demonstration on Mars 2020
FISO Telecon 03-20-2019
Joint effort of Jet Propulsion Laboratory, NASA Ames Research Center, NASA Langley Research Center, and AeroVironment

## Slide 2
Aerial Dimension:
Bridges gap between orbital and ground-level imagery
(Illustration)

## Slide 3
Aerial Dimension:
Scouts terrain far ahead of rovers, and possibly someday, humans
(Illustration)

## Slide 4
Aerial Dimension:
Goes where it is inaccessible for rovers or humans
(Illustration)

## Slide 5
Co-axial rotor configuration
Blades 1.2-meter tip-to-tip
Mass ~1.8 kg
Battery powered
Recharges using solar panel
Mars Helicopter Technology Demonstrator

## Slide 6
Demonstration Flights at Mars

## Slide 7
Challenges
Launch loads
Vacuum compatibility
Temperature extremes
Planetary protection
Radiation
No global navigation aids
Large communication lag with Earth
Extremely thin atmosphere
  Only 1-2% of Earth density
  Partially “offset” by lower gravity (38% of Earth)
  Density equivalent to ~100,000 feet above sea level

## Slide 8
Basic Scaling
Rotor size R limited by accommodation constraints (R = 0.605 m)
Density ρ is ~1% of Earth (ρMars = 0.01 ρEarth)
Speed of sound c is approximately 76% of Earth (cMars = 0.76 cEarth)
Gravity g is 38% of Earth (gMars = 0.38 gEarth)
Max rotor speed Ω is limited by tip Mach number
  Max speed for given rotor size: ΩMars = 0.76 ΩEarth
Thrust scales T as Ω2ρ
  Max thrust for given rotor size: TMars = 0.006 TEarth
Mass m scales as T/g
  Max vehicle mass for rotor size: mMars = 0.015 mEarth
For given mass and rotor size, ideal hover power P scales as g3/2/ρ1/2
  Ideal power for given mass/rotor size: PMars = 2.34 PEarth

## Slide 9
The Big Picture
Mass and power are primary design drivers
Big and fast rotor + small fuselage
Batteries will take up much of the available mass
Very little mass available for everything else

## Slide 10
    Question: Can helicopter flight be achieved on Mars?

## Slide 11: Early Test in Mars Atmosphere (2014)

## Slide 12
    Question: Can controlled helicopter flight be achieved on Mars?

## Slide 13: Controlled-Flight Demonstration Effort
Eight-month effort in 2015-2016 to demonstrate controlled flight in Mars atmosphere with full-size rotor
Driven heavily by flight dynamics modeling
Key insight: helicopter must be built for controllability
Early model of open-loop response

## Slide 14: Helicopter is Controlled with Variable Pitch
Increased pitch
Increased lift
Pitch controlled with servos
that move swashplates
Servo
Swashplate
Relative wind
Lift
Airfoil section
Drag
Lift
Relative wind
Drag

## Slide 15: Types of Pitch Variation
Collective control
Changes average blade pitch
Cyclic control
Changes blade pitch periodically
Increases lift on one side
Decreases lift on other side
Pitch up
Pitch down
Pitch up
Pitch up

## Slide 16
Coax Control
Upper/lower collective input in opposite directions
Cyclic input
Tilted helicopter gains forward velocity
Upper/lower collective input in same direction

## Slide 17: Flap Dynamics
Blade flapping similar to mass-spring-damper
Reduced damping on Mars changes response
  In particular to periodic inputs – cyclic control and wind/gusts
Introduces highly oscillatory modes
  Problematic for control
Mitigation: make rotor very stiff
  80-90 Hz rotating flap frequency
  Custom blade design using foam core with carbon fiber skin
Earth example
Mars

## Slide 18
Full-Sized Rotor Mars Helicopter Prototype
Electrical cables
1.2 meter Diameter Rotors
Visual targets for Motion Tracking
Landing legs
Motor, gears &
pitch linkages Assembly
Counter-rotating Rotors
Safety tether
(removed for free-flight)

## Slide 19: Path to Controlled Flight
Modeling and simulation
Free flight
System identification
Attitude Control
Vehicle Design

## Slide 20: Swinging Arm Sys-ID

## Slide 21: First Free Flight

## Slide 22: Flight Design
Main features of demo vehicle retained
Much heavier vehicle (1.8 kg)
  Batteries, solar panel, avionics, sensors, etc.
Enabling factor: lightweight COTS technology
  Batteries, avionics, sensors
  Largely developed for cell phone and drone markets
Landing System
Rotor System
Telecom
Solar Panel
Fuselage
Avionics Processing
Sensors & Cameras
Battery

## Slide 23
Rotor System
Identical upper and lower rotor
Collective -4.5˚ to 17.5˚
Cyclic -10˚ to +10˚
Carbon fiber composite
Maxon servo motors
Custom brushless drive motors with co-located drive electronics

## Slide 24
Landing Gear
Folded and deployed
Lightweight carbon fiber
Damping through deformable aluminum flexure
Ensures landing safety up to 2 m/s vertical contact velocity
Deployment hinge and latch
Aluminum damper
Carbon fiber landing leg
Titanium flexure
Clevis and interface plate
Foot
Leg
Deployment hinge and flexure/damper mechanism
Interface plate

## Slide 25
Avionics & Communications
COTS parts selected for thermal and radiation tolerance with additional custom mitigations as needed
Computing
Radiation tolerant FPGA
Redundant “hot swap” of flight controllers
High-Level navigation processor
Communications
Zig-Bee (802.15.4) protocol standard 900 MHz radio two node network

## Slide 26
Power, Energy & Thermal
Solar Panel
Inverted Metamorphic Quadruple Junction (IMM4) solar cells
Tuned for Mars spectrum
Battery
Lithium ion
6 Sony VTC4 cells
510 W Peak Power
Thermal System
CO2 gas-gap insulation
Survival heaters
High alpha fuselage coating
Low-conductivity composites
Optimized wire gages

## Slide 27
Electronics

## Slide 28
Sensors
IMU (Bosch Sensortec BMI-160)
Inclinometer (MEMS MuRata SCA100T-D02)
Altimeter (Garmin Lidar-Lite-V3)
Navigation (NAV) Camera (640 by 480 pixel Omnivision OV7251)
Return-to-Earth (RTE) Camera (4208 by 3120 pixel Sony IMX 214)
Bosch BMI-160 IMU
Garmin Lidar-Lite-V3
Altimeter

## Slide 29: Guidance and Control
Classical nested control architecture: outer position loop around inner attitude loop
Guidance plans smooth trajectories between ground-provided waypoints
Takeoff strategy
“Jump” off ground with fixed thrust and limited control
Switch to full control after separating from ground
Landing strategy
Fly toward ground at constant speed
Switch off control when ground contact detected
  As indicated by control residuals

## Slide 30: Navigation
Based on feature detection and tracking
  FAST + KLT algorithms at 30-Hz frame rate
Features mapped onto ground plane
  Assumed known
Mapped feature locations compared to predicted locations
  Residuals used as filter innovations in Extended Kalman Filter

## Slide 31
Rover Accommodation
Base Station Electronics
Base Station Antenna
Mars Helicopter (stowed)
Mars Helicopter Delivery System

## Slide 32: Flight Control Testing and V&V
System identification
Control design &
robustness verification
Flight simulation
Navigation testing
Closed-loop testing
Integrated flight testing

## Slide 33: System Identification
Multiple configurations
  Fixed on F/T sensor, swinging arm, gimbal
Forward flight testing using purpose-built wind wall
  ~900 CPU-type fans
  Up to ~11 m/s

## Slide 34: Navigation Testing
Outdoor testing with surrogate platform
Achieves sufficient photorealism
Space for large maneuvers
34

## Slide 35: Flight Simulation
Simulations performed using HeliCAT
Flight software in the loop
Monte-Carlo variations

## Slide 36: Flight With Onboard Navigation

## Slide 37
ORBITERS
Wide-Area
Lower-Res Imaging
LANDERS
Single Location
No Mobility
Local High-Res Imaging
ROVERS
Limited Mobility
Local High-Res Imaging
ROVER PAIRED WITH SCOUT
Efficient Mobility
Wide-Area High-Res Imaging
Opening Doors to New Classes of Exploration
INDEPENDENT
HELICOPTER SCOUT
Long-Range Mobility
Wide-Area High-Res Imaging
REGIONAL EXPLORATION USING MULTIPLE HELICOPTERS
BIOLOGICALLY SENSITIVE ZONE EXPLORATION
Pre-decisional information – for planning and discussion purposes only